## Slide 1: Agricultural Water Transfers in Northern California and Implications for Sustainable Management of Groundwater Storage
Steffen Mehl & Eric Houk
Kyle Morgado, Kevin Anderson, and Jeff Davids
CSU Chico
Funding by:
USBR, USDA, & CSU Agricultural Research Institute

## Slide 2: Outline
Overview of CA water
Water transfers to balance CA’s water budget
  Effects of water transfers on groundwater
Compare surface vs. groundwater storage
Concepts of capture and groundwater management
  Lake Tahoe Analogy

## Slide 3: CA has a lot of water, right?

## Slide 4: California Water
Source: Justin Sullivan/Getty Images
Notes: Governor Brown showing statewide precipitation by water year from 1970 through 2014. Shows the extreme variability in precipitation which highlights the importance of sufficient storage.

## Slide 5
Precipitation
  North vs. South
Stream flows
  North vs. South

## Slide 6: California Water
California’s climate is characterized by extremes
Mismatch between supply and demand (spatially and temporally)
  2/3 of demand in the south
  2/3 of supply in the north
  Peak precipitation from November to April
  Peak demand from May to October

## Slide 7: Drought Management

## Slide 8
Lake Oroville
July 20, 2011
August 20, 2014

## Slide 9
Variability in Precipitation
Coefficients of variation of Total Precipitation, 1951-2008;
Dettinger et al. 2011
Notes: Coefficients of Variation of Total Precipitation, 1951-2008 (Dettinger et al. 2011)

## Slide 10
Timing of Precipitation
Number of days to accumulate 67% of annual total precipitation;
Dettinger et al. 2011
Notes: CA accumulates 2/3 of its total precipitation in less time than any other state (<125 days), indicating a far shorter wet season

## Slide 11: California’s Water Supply Issues
High variability = high uncertainty = low reliability
In times of drought we turn to groundwater
Groundwater pumping was unregulated
  Unlike surface water which is highly regulated
    Prior appropriations (senior water rights)
  Pre-SGMA legal framework for managing groundwater:
    Whoever has the biggest/deepest well wins!

## Slide 12: Types of Water Transfers Considered
Groundwater Substitution
  Farmers sell (transfer) their surface water
  Pump groundwater to offset loss of surface water
  Controversial because pumping can affect other users
Land Fallowing with Surface Water Transfer
  Rice acreage is fallowed
  No additional groundwater is pumped
  No application of surface water to land
  Does lack of excess irrigation affect aquifer recharge?

## Slide 13: Groundwater Substitution Scenarios
Pumping for transfers
  75,000 acre-ft/yr up to
  600,000 acre-ft/yr
  1 year of pumping, 9 years recovery

## Slide 14: Aquifer Decline
75,000 AF scenario
600,000 AF scenario
Drawdown in Feet

## Slide 15: Land Fallowing of Rice Fields
Rice is flood irrigated with surface water
  ~5 ft of water per acre of rice
Rice field is fallowed and water is transferred
Effect on recharge?
Notes: Figure from CA water plan

## Slide 16: 10 Years of Rice Land Fallowing
Folsom Lake

## Slide 17: Groundwater Depletion & Sustainability
Measured from space by GRACE (Gravity Recovery and Climate Experiment)
  Good news: this method works!
  Bad news: indicates we are running out of groundwater!
Cumulative GW loss in California’s Central Valley
Notes: Figure from Famgalletti. http://newswatch.nationalgeographic.com/2014/02/04/epic-california-drought-and-groundwater-where-do-we-go-from-here/
From Sandra Postel:
http://newswatch.nationalgeographic.com/2014/07/30/groundwater-depletion-in-colorado-river-basin-adds-big-risks-to-water-security/
Imagine having a bank account for which you don’t know (1) how much money is in the account, (2) how much gets withdrawn, or (3) how much will get deposited, or when.
Figure from UCCHM Water Advisory #1. Cumulative groundwater losses (cubic km and million acre-ft) in California’s Central Valley since 1962. The red line shows data from USGS calibrated groundwater model simulations from 1962-2003. The green line shows satellite-based estimates of groundwater storage losses produced by the UCCHM at UC Irvine. Background colors represent periods of drought (white), of variable to dry conditions (grey), of variable to wet conditions (light blue) and wet conditions (blue). Groundwater depletion mostly occurs during drought; and progressive droughts are lowering groundwater storage to unsustainable levels. After Figure B9 from USGS Professional Paper 1766. USGS data courtesy of Claudia Faunt. Satellite data courtesy of NASA and the National Center for Atmospheric Research.

## Slide 18: 2014 Sustainable Groundwater Management Act (SGMA)
Motivations for passage of SGMA
  Increasing agricultural, municipal, and environmental demands for water
  Persistent overdraft and land subsidence
  Rising concerns over the impending effects of climate change on California’s water supply
  Increasing evidence of the interconnections between surface water and groundwater
  Ongoing severe drought conditions

## Slide 19: Relative Merits of Groundwater vs. Surface Water (adapted from Harvey)
Surface Reservoirs
Subsurface Reservoirs
Disadvantages
Advantages
)
Few new sites available
(USA
Many large capacity sites available
High evaporative losses
Practically
no evaporative loss
Need
large areas of land
Need very small areas of land
May fail catastrophically
Practically
no danger of failure
Easily
polluted
Usually high biological purity,
although pollution can occur
for
Water
must be conveyed
Internal conveyance (no need
canals)
Notes: Adapted from Harvey

## Slide 20: Management of Groundwater vs. Surface Water
Surface Reservoirs
Subsurface Reservoirs
Advantages
Disadvantages
Well
defined boundaries
Boundaries often unknown
High
rates of flow possible
Limited rates of extraction/injection
Only 1 measurement needed
Need many measurements in space
Responds
as a level pool
Response
depends on location and
can be nonlinear
Response time is relatively fast
Response time is relatively
slow
Well defined
conveyance
system
Internal
conveyance

## Slide 21: Theis Concept of Capture
“All water discharged by wells is balanced by a loss somewhere.” – Theis, 1941
  Storage, induced recharge, reduced discharge (capture)
Notes: From a USGS Circular – Surface – Groundwater a single resource
Recent work (Konikow and Leake) indicate that most of the water from wells is not from storage (15%), but rather capture (85%)

## Slide 22: Stream/Aquifer Interactions
Source: The Nature Conservancy

## Slide 23: Sustainable Management Metrics
Adverse impacts Subsidence:
  Extremely important
    By the time it is measured, it’s too late (if inelastic)

## Slide 24: Sustainable Capture Concepts
Apply concepts of capture to each discharge flow path
SCF = Sustainable Capture Fraction
  Stakeholder driven process
    Fraction of flow path that can be “sustainably” captured?
    Ranges between 0 and 1
SCT = S (SCF*discharge)= rate of sustainable extraction
Capture Efficiency: Ratio of the actual amount of discharge captured over the SCT

## Slide 25: Example
0.14 m3/s
0.14 m3/s
??
m3/s
0.28 m3/s
??
m3/s
0.2035 m3/s
0.2035 m3/s
Phreatophytes 0.26 m3/s
Stream outflow 0.30 m3/s
Given the discharge, stakeholders decide:
  Need to keep at least 0.15 m3/s in the stream
  Okay to deplete phreatophytes
Proposed GW pumping
= 0.407 m3/s

## Slide 26: Management After Overdraft
Consider 15 years of over pumping
How should pumping be changed for sustainability?
  Adaptive management based on:
    Water budget over draft
    Capture

## Slide 27
Chart: Q = 0.407 m3/s (Wells 1.5 km from Stream)
SW_Captured | 0 | 0.069292 | 0.11975 | 0.15355 | 0.17748 | 0.19563 | 0.21011 | 0.22206 | 0.23212 | 0.24065 | 0.24798 | 0.25429 | 0.25972 | 0.26443 | 0.26853 | 0.2721 | 0.27518 | 0.27787 | 0.28016 | 0.28212 | 0.28382 | 0.28531 | 0.28659 | 0.28771 | 0.28869 | 0.28955 | 0.2903 | 0.29096 | 0.29153 | 0.29204 | 0.2924
ET_Captured | 0 | 0.0074455 | 0.019413 | 0.031554 | 0.04239 | 0.051722 | 0.059719 | 0.066562 | 0.072476 | 0.077553 | 0.081941 | 0.085762 | 0.089082 | 0.091958 | 0.094467 | 0.096661 | 0.098583 | 0.10027 | 0.10176 | 0.10307 | 0.10424 | 0.10527 | 0.10619 | 0.10701 | 0.10774 | 0.10839 | 0.10898 | 0.10951 | 0.10999 | 0.11043 | 0.11087
Threshold exceeded
by 0.14 m3/s
Halt Pumping
>1.5 year residual effect
Pumping reduced by 0.14 m3/s
Pumping reduced considering capture
Threshold exceeded
Adapt after 5 years
Reduce pumping by 0.067 m3/s

## Slide 28: Sustainable Groundwater Storage vs. Surface Storage
Storage depleted less than 1% of total groundwater storage
  Unlike reservoirs
Lake Tahoe
  Only upper few feet can be sustainably exercised
  Advantage that changes in lake levels are easily observed and impacts to outlet flows are immediate

## Slide 29: Sustainable Management Metrics
Need metrics that are:
  Flexible
    SW/GW interactions are complex, integrated systems
    Spatial/temporal variability in SW/GW interactions
  Meaningful
    Represent effects on SW/GW in a hydraulically correct way
    Can be incorporated into a management framework
  Easily Understood
    Many stakeholder with varied technical knowledge

## Slide 30: Conclusions Storage, Capture, and Sustainable Yield
Managing groundwater storage requires a different framework than surface water storage
    Need to manage effects of capture on streams
Sustainable yield in stream/aquifer systems
  Sustainable groundwater storage often is a small % of total groundwater storage
  Stream/spring flows are the “canaries in the coalmine”
Notes: Maybe save some of this for conclusions.