## Slide 1: Evaluating and enhancing groundwater recharge in the Sacramento area
Amelia Vankeuren
Assistant Professor of Geology
CSU Water Resources and Policy Initiatives Annual Conference
19 April 2019

## Slide 2: Acknowledgements
Collaborators:
Ate Visser, Lawrence Livermore National Lab
Sacramento State Geology students:
Marissa Loustale, Amber Ginorio, Austin George, Adelia McGregor, Jack Shafer, Brian Clark, Nick Rice
Support for this work was provided by:
UC California Institute for Water Resources through a grant agreement with the United States Geological Survey
Sacramento State Research and Creative Scholarly Activity Faculty Awards program
Lawrence Livermore National Laboratory Glenn T. Seaborg Institute Nuclear Forensics Summer Internship Program
Sacramento County Water Agency
The Nature Conservancy
City of Sacramento Water Forum

## Slide 3: Road map
Part 2
Enhancing recharge through off-season irrigation
Part 1
Quantifying natural groundwater recharge with climate change

## Slide 4: California’s groundwater bank account

## Slide 5: Precipitation- and surface water availability- is highly variable
WestMap Climate Analysis and Mapping Toolbox. Desert Research Institute. Accessed 2/25/18.
1900
2020
1980
1940
20
30
10
Year
Statewide water year precipitation (in)
40
average
4 fold difference between
minimum and maximum annual inflows
minimum
maximum

## Slide 6: Climate change is predicted to shift snowpack and cause more extreme weather events
Photos from Rich Pedroncelli/AP; Justin Sullivan/Getty Images
Lake Oroville
2014
2017
2015

## Slide 7: Quantifying natural groundwater recharge at the Sacramento State Campus Well Field
Figure 2. Map created in GIS to indicate location of well on campus.
Figure 2. Map created in GIS to indicate location of well on campus.
Monitoring wells
13 in unconfined aquifer
6 in confined aquifer
1 Extraction well
American River

## Slide 8: Sacramento State Campus Well Field
Levee with slurry wall
M
S
S
Lower American River
D
D
200 ft
2200 ft
Confined Aquifer
Confining Layer
Unconfined Aquifer
Modified from image provided by Adelia McGregor, CSUS Geology student

## Slide 9: Groundwater in both aquifers flows southwest away from the Lower American River
Figure 2. Map created in GIS to indicate location of well on campus.
Figure 2. Map created in GIS to indicate location of well on campus.
Figure 10: 2016 Unconfined groundwater surface contours
Figure 9: 2016 Confined groundwater surface contours
Figure 10: 2016 Unconfined groundwater surface contours
Figure 9: 2016 Confined groundwater surface contours
Water level (ft) above sea level
Unconfined aquifer
Confined aquifer

## Slide 10: Groundwater sampling and geochemical characterization
Left: Photo by Fatima Burhan. CSUS Geology undergraduate students and faculty, and LLNL scientist sample groundwater from monitoring wells.
Above: CSUS Geology undergraduate student performing groundwater chemical analyses

## Slide 11: Most water in campus aquifers is from the American River
Figure 2. Map created in GIS to indicate location of well on campus.
Wells with mixed river water and local precipitation
Wells with mostly river water
Modified from Loustale et al. (2017), American Geophysical Union Fall Meeting
Stable isotopes ∂2H (‰)
Stable isotopes ∂18O (‰)

## Slide 12: In the shallow aquifer, groundwater age increases along vertical flowpath
Older
Recharge from land surface infiltration
0.3 -0.7 ft/yr
water table
Recharge from American River
24 ft/yr
Older

## Slide 13: In the deeper confined aquifer, groundwater age increases along horizontal flowpath
Older
Recharge from river water
11 ft/yr
All wells at ~200 ft depth
Older

## Slide 14: Quantifying recharge to the groundwater system
Recharge from river water
4 - 11 ft/yr
50 acre-ft/yr
Older
Older
Recharge from land surface infiltration
0.3 - 0.7 ft/yr
100 acre-ft/yr
Recharge from river water
24 ft/yr
500 acre-ft/yr
Older

## Slide 15: In this dam-controlled system, groundwater recharge will occur even in drought years
Summer flows for Central Valley Project

## Slide 16: Precipitation will vary depending on how the climate changes
Annual precipitation (in)
40
20
30
2020
2030
2025
2035
10
Data from Cal-Adapt.org
Less warm/
Less dry
Warmer/
Drier
average

## Slide 17: American River discharge will vary depending on how the climate changes
2020
2030
2025
2035
10
5
6
7
8
9
American River Stage (m)
Cooler/
Wetter
Warmer/
Drier

## Slide 18: So how much will recharge vary with climate change?

## Slide 19: So how much will recharge vary with climate change? Modeling predicted recharge in Sacramento
Sacramento State campus
American River
Sacramento River
Model area

## Slide 20: Enhancing recharge: Off-season irrigation of crops for managed aquifer recharge
Photo by Josh Viers, in O’Geen et al. (2015), California Agriculture (69)2
Water table

## Slide 21: Off-season irrigation of vineyards along the Cosumnes River corridor
785 acres
376 acres
89 acres
Google Earth
Collaborators
Omochumnee-Hartnell Water District/ Larry Walker Assoc.
UC Davis Hydrology
Cosumnes Coalition
Notes: 1250 acres

## Slide 22: Off-season irrigation of vineyards along the Cosumnes River corridor
Plan to recharge 4,000 – 6,000 acre-ft/year for 10 years
Irrigation will occur November– March when excess water flows in Cosumnes River
Actual amount will depend on water availability
Photo by Paul Verdegaal, in O’Geen et al. (2015), California Agriculture (69)2

## Slide 23: Monitoring groundwater quality and flow direction
Photo by Melinda Frost-Hurzel. CSUS Geology graduate student and faculty test wells at Teichert Ranch for groundwater sampling
Water quality
Do fertilizers and pesticides get washed down with the recharge water?

## Slide 24: Monitoring groundwater quality and flow direction
https://gis.water.ca.gov/app/gicima/
Water quality
Do fertilizers and pesticides get washed down with the recharge water?
Where does the groundwater go from here?
?
?

## Slide 25: Background sampling

## Slide 26: Can we do enough managed aquifer recharge to offset overdraft?
2.7 million acre ft/yr of river water high flows in the Central Valley that could be harvested and stored
Could add 6% to the annual water supply
That’s about the same volume as annual groundwater overdraft
Would need to store every drop of extra river water to offset overdraft
Kocis and Dahlke (2017), Environmental Research Letters
Notes: Is it realistic to think we can harvest all excess flows? Probably not.

## Slide 27: Can we do enough managed aquifer recharge to offset groundwater overdraft?
O’Geen et al. (2015), California Agriculture (69)2
Statewide:
Areas in California with good managed aquifer recharge potential are mostly in the south
But available water is mostly in the north
Would need infrastructure to bring the water to the appropriate locations
California Precipitation, US Geological Survey National Atlas
Notes: Is it realistic to think we can harvest all excess flows? Probably not.

## Slide 28: Conclusions
Lower American River supplies 85% of campus groundwater
East Sacramento unconfined aquifer is recharged by a mixture of American River water and local precipitation
Confined aquifer is recharged by American River water
Climate change will alter natural recharge, but by how much?
Enhancing recharge through off-season irrigation will help achieve groundwater sustainability, but is no silver bullet

## Slide 29: Questions?
Lower American River supplies 85% of campus groundwater
East Sacramento unconfined aquifer is recharged by a mixture of American River water and local precipitation
Confined aquifer is recharged by American River water
Climate change will alter natural recharge, but by how much?
Enhancing recharge through off-season irrigation will help achieve groundwater sustainability, but is no silver bullet